## Slide 1: Socket Communication Using Cavli C10GS Module
SANITTA TREESA SONY

## Slide 2: AT COMMANDS
  AT+QICSGP=1,1,"apn","","",1 → Set APN
  AT+QIACT=1 → Activate PDP
  AT+QIOPEN=1,0,"TCP","host",port,0,1 → Open socket
  AT+QISEND=0 → Send data
  AT+QICLOSE=0 → Close socket

## Slide 3: EXAMPLE
APN CONFIGURATION
  AT+QICSGP=1,1,"airtelgprs.com","","",1 OK
  1: Context ID
  “airtelgprs.com”: APN
  Last ‘1’: IPv4 protocol
ACTIVATE PDP CONTEXT
  AT+QIACT=1 OK
  Activates the internet session

## Slide 4: EXAMPLE
OPEN TCP SOCKET
  AT+QIOPEN=1,0,"TCP","example.com",80,0,1 OK +QIOPEN: 0,0
  Connects to server on port 80 (HTTP)
  1 = context ID
  0 = socket ID
  “TCP” = protocol
  “example.com” = remote host
  80 = port number
  Last values = keep-alive and service type
SEND DATA
  AT+QISEND=0,19 > GET / HTTP/1.1\r\n\r\n Response: SEND OK
  0 = socket ID
  19 = number of bytes to send
  Waits for > prompt, then user sends HTTP GET or any data
CLOSE SOCKET
  AT+QICLOSE=0 CLOSE OK

## Slide 5: SUMMARY
Command | Purpose
AT+CGDCONT: | Set APN and PDP context
AT+QIACT : | Activate data context
AT+QIOPEN : | Open TCP socket
AT+QISEND : | Send data to server
AT+QICLOSE : | Close socket connection

## Slide 6: FLOW IN REAL MODEM
  Check SIM: AT+CPIN?
  Check signal: AT+CSQ
  Attach to network: AT+CGATT=1
  Configure APN: AT+QICSGP=...
  Activate PDP: AT+QIACT=1
  Open socket: AT+QIOPEN=...
  Send data: AT+QISEND=0
  Close: AT+QICLOSE=0